## Slide 1
Creative Coding Club
Free IoT Practical Coding Workshop 4

## Slide 2
Meetup Hosts
Dipto Pratyaksa
Raymond Chan
Looking for volunteer co-hosts and speakers

## Slide 3
How are we different?
No specific technology / platform
Very practical, focus on software development
A coding dojo
Mini hackhathons
Cross expertise

## Slide 4
Free Workshop series
11/2/2018 Club established
25/2/2018 IoT workshop 1 Arduino & breadboards
11/3/2018 IoT workshop 2 Arduino & breadboards
25/3/2018 IoT workshop 3 ESP8266 & wifi
Today
8/4/2018 IoT workshop 4 ESP8266 & wifi
Next meetups
22/4/2018 IoT workshop 5 Controlling IoT via phones
6/5/2018 IoT workshop 6 Python and data

## Slide 5
Courses in May 2018
Arduino and electronics prototyping class
  1 day class $99 / person
  4 hours of lesson, hands on exercise, and group discussion
  Arduino kit, breadboards, and basic electronic components kit
  Sample codes
  Class notes
IoT fundamental class
  1 day class $99 / person
  4 hours of lesson, hands on exercise, and group discussion
  ESP8266 kit and breadboards, and basic electronic components kit
  Sample codes
  Class notes

## Slide 6
Workshop #4 Today’s Agenda
1.00 Creative Coding Club Raymond
1.15 Past workshops recap Raymond
1.45 NodeMCU ESP8266 Dipto
2.00 Build and Code All
3.00 Meetup concludes All

## Slide 7
House Keeping OH&S
Emergency exit, toilets
Safety:
  Always disconnect power before you modify electronic components
  Never short-circuit: Red wire + black wire = FIRE!
  Reverse polarity = FRIED BOARD
  Check and double check your wiring
  In case of incident, switch off power supply, ask for help

## Slide 10
Source: Deloitte website

## Slide 15
The Breadboard - Horizontal Columns

## Slide 16
The Breadboard - Vertical Columns

## Slide 17
Code Overview
Arduino Sketch
  A sketch is the name that Arduino uses for a program. It's the unit of code that is uploaded to and run on an Arduino board.
  C/C++ codes with pre-built libraries
  https://www.arduino.cc/en/Tutorial/Sketch
Arduino Genuino IDE
  Code
  Verify
  Upload
  https://www.arduino.cc/en/Guide/Environment

## Slide 18
Typical code structure
setup()
loop()

## Slide 19
Arduino Serial Communications
How to 'talk' to this thing?
http://www.ladyada.net/learn/arduino/lesson4.html

## Slide 20
Sending data wireless: RF
RF transmitter and receiver 433Hz

## Slide 21
Sending data wireless: Bluetooth

## Slide 22
Sending data wireless: Wifi

## Slide 23
Open-source and open hardware IoT solutions

## Slide 24
NodeMCU ESP8266 Class

## Slide 25
What is the ESP8266?
Microprocessor and WIFI board
Full TCP/IP stack
32-bit RISC microprocessor
16 GPIOs
Less than $4
Perfect for IOT projects

## Slide 27
What is the NodeMCU?
Development board for the ESP8266
USB Programmable
Easier to use
More expensive, wouldn’t be used for mass production, just for prototyping

## Slide 28
What We’re Building
A simple circuit that controls an LED over WIFI, showing you how to do output over wifi
A simple circuit that read a light sensor (photoresistor) over wifi, showing you how to read input over wifi
Together these are the basic tasks you’ll want to do with an IOT project, input and output over the air

## Slide 29
What’s in the kit?
NodeMCU ESP8266 Development Board
MicroUSB Cord
Breadboard
LED
Photoresistor
10K Resistor
4 Jumper Wires

## Slide 30
How to program it?
A few different ways supported by the community
Some people use LUA programming language
Community and company put out IDE’s
We’ll be using C++ and Arduino IDE for simplicity

## Slide 31
Setting Up The Environment
Install Arduino IDE
  Google “Install Arduino IDE”
  Download the installer & run it
Setting Up ESP8266 for Arduino IDE
  File -> Preferences
    Additional Boards URL: http://arduino.esp8266.com/stable/package_esp8266com_index.json
  Tools -> Boards -> Boards Manager
    Search “ESP8266” & Install the board
Select the board
  Tools -> Boards -> NodeMCU 0.9 (ESP-12 Module)
Select COM Port
  Tools -> Port -> COM#

## Slide 32
Setting Up The Environment Continued
Change Serial Monitor BAUD Rate
  Tools -> Serial Monitor
  From new window: 115200 BAUD
  This allows NodeMCU to communicate with your computer

## Slide 33
Hooking up the Circuit
LED Circuit
  Put the NodeMCU at the top of the breadboard
  Connect GND to the right – rail
  Connect 3v3 (row 10) to row 20
  Connect LED’s anode (long pin) to row 20, and the cathod to the – rail
  Connect Pin D7 (row 6) to row 27
Photo resistor Circuit
  Connect the photoresistor to row 27 and row 29
  Connect pin A0 (row 15) to row 29
  Connect the 10K resistor to row 29 to the - rail

## Slide 34
The Code and this slide
Put in a folder called NodeMCU_IO_Tutorial
https://github.com/elmtreecomputers/nodemcu_tutorial

## Slide 35
Reference and resources
Arduino and circuits
  https://www.allaboutcircuits.com/projects/learn-how-to-use-the-arduinos-digital-i-o/
  https://www.makeuseof.com/tag/getting-started-with-arduino-a-beginners-guide/
  https://computers.tutsplus.com/tutorials/how-to-use-a-breadboard-and-build-a-led-circuit--mac-54746
  www.Arduino.cc
Design thinking process:
  https://www.youtube.com/watch?v=qyoZTUGzdGY

## Slide 36
Next Meetup
Sunday 8 April 1-3pm
OfficeWorks Carnegie
Topics:
  Further wireless communications
  Connecting ESP8266 with a mobile phone
  JavaScript